## Slide 1
GITAM (Deemed-to-be) University
www.gitam.edu
Department of Electrical Electronics and Communication Engineering
Project Team:
Monisha H S – BU22EECE0100439
Prajwal Shetty – BU22EECE0100434
Project Mentor:
Mr. Kshitij Shakya
Project In-charge:
Mr. Shatadal Chatterjee
Ear-Wearable SpO₂ and Heart-Rate Monitoring Device for Low-Ventilation Area Workers
Review-I
AY 2025-26
Capstone Project – Introduction (PROJ2999)

## Slide 2
Objective and Goals
Objective
Goals
This project aims to develop a compact ear-wearable device that continuously measures blood oxygen saturation (SpO₂) and heart rate of workers in low-ventilation environments such as mines, tunnels and factories.
Using a MAX3010x optical sensor mounted in an ear clip and a microcontroller (Arduino/ESP32), the system acquires photoplethysmography (PPG) signals from the ear.
A simple AI/ML algorithm analyses the signals in real time to distinguish genuine drops in SpO₂ from motion artefacts, and triggers LED/buzzer alerts only when a verified low-oxygen event occurs.
The goal is a portable, comfortable and reliable safety monitor that reduces false alarms while improving worker health monitoring.
Main Goals
Develop hardware prototype using MAX3010x sensor and Arduino/ESP32
Collect and analyze PPG signals from the ear and Train ML models for noise removal & anomaly detection
Provide real-time alerts via buzzer/LED for safety and Ensure comfort and portability for continuous use
Additional Goals
Add wireless/cloud connectivity for supervisor monitoring
Optimize power consumption for longer operation
Create a dashboard/app for real-time visualization of workers’ vitals

## Slide 3
Project Plan
Review | Objectives | Milestones
Review I | Conduct literature survey on wearable SpO₂ devices and PPG processing. Select hardware components (MAX3010x sensor, Arduino/ESP32, ear-clip design). Collect or prepare PPG data in Python for signal analysis practice. | Literature survey completed. Hardware components finalized. PPG data collected (simulation yet to be run).
Review II | Integrate MAX3010x sensor with Arduino/ESP32. Continue data collection from volunteers to get real PPG signals. Train initial ML models for noise removal and anomaly detection. | Hardware integration planned. Volunteer data collection ongoing. Initial ML model training scheduled.
Review III | Assemble final ear-wearable prototype with ergonomic design. Perform testing & validation in simulated low-ventilation conditions. Prepare presentation of results and outline future scope. | Final prototype to be ready for demonstration. Test results to be documented. Presentation & future roadmap to be prepared.

## Slide 4
Literature Survey
Key Publications (IEEE & Scholarly Papers)
Photoplethysmography Signal Processing for Wearable Health Monitoring – Techniques for accurate PPG signal analysis in wearables
Machine Learning Algorithms for Real-Time SpO₂ Monitoring in Wearable Devices – ML approaches to improve SpO₂ measurement reliability
Comparative Study of Finger and Ear-Based SpO₂ Measurement Techniques – Evaluates accuracy and advantages of ear-based sensors over finger sensors
Key Resources (Datasheets / Whitepapers / Application Notes)
MAX3010x datasheet – sensor specifications and integration details (Maxim Integrated)
Integration guide for MAX3010x in wearable devices
Signal processing techniques – methods to filter noise and motion artefacts from PPG signals
Existing Implementations
Products:
Oxi Wear – FDA-approved ear-worn pulse oximeter for continuous monitoring
Open-Source / GitHub Projects:
Arduino MAX3010x libraries – for interfacing the sensor with Arduino
Ear-wearable PPG sensor projects – reference projects demonstrating ear-based SpO₂ monitoring

## Slide 5
Architecture
Structural Diagram
Block Diagram/Pin Diagram
Behaviour Diagram
Flow chart/ State machine

## Slide 6
Use Cases & Testing
Use Cases
Industrial Safety Monitoring: Continuous SpO₂ and heart rate tracking for workers in mines, tunnels, and low-ventilation factories.
Preventive Alerts: Early warning when oxygen saturation drops below safe levels.
Portable Health Device: Comfortable ear-wearable design for real-time monitoring during long shifts.
Data Logging & Analysis: Storing physiological data for supervisors to assess worker health trends.
Research / AI Development: Dataset creation for machine-learning models to improve accuracy of wearable PPG-based devices.
Testing Approach
Hardware Testing: Verify sensor (MAX3010x) accuracy by comparing with a commercial pulse oximeter. Check ear-clip stability and comfort for different users.
Signal Processing Testing: Test filtering methods to remove noise/motion artefacts. Validate feature extraction (SpO₂, heart rate) with sample datasets.
Machine Learning Testing: Train and test models on collected PPG data. Evaluate performance using metrics: accuracy, sensitivity, specificity.
System Testing: Simulate low-oxygen environments and check real-time alert response. Test wireless transmission (if used) for data integrity. Conduct pilot testing with small group of volunteers.

## Slide 7
Implementation and Results – Iteration 1
Iteration 1 : Results
Implementation:
Completed detailed literature survey on wearable SpO₂ sensors and ML approaches.
Finalized component selection → MAX30100/30102 sensor + Arduino/ESP32.
Designed system architecture (block diagram + flow chart).
Identified ML approach (classification model for anomaly detection).
Results:
Validated that ear-based SpO₂ monitoring is feasible and more stable than finger sensors (from references).
Confirmed design feasibility for industrial use case.
Reviewed public PPG datasets for training reference.
Defined clear roadmap for hardware setup.

## Slide 8
Implementation and Results – Iteration 2
Iteration : Results + Validation against the use cases and test cases
Implementation (Planned):
Integrate MAX30100/30102 with Arduino/ESP32 for live data acquisition.
Apply preprocessing & filtering on raw PPG signals.
Extract features: SpO₂ percentage, heart rate, pulse rate variability.
Implement basic ML classifier for anomaly detection.
Results (Expected):
PPG Signal Dataset Collected → from ear sensor under normal & simulated low-ventilation conditions.
Accuracy Check → SpO₂ values validated against commercial finger oximeter.
Noise Reduction → Filtering improves clarity and stability of PPG waveforms.
Prototype Demonstration → Device gives alert (LED/Buzzer) when SpO₂ < threshold.
Validation Against Use Cases & Test Cases:
The prototype supports continuous worker safety monitoring, provides preventive alerts below safe SpO₂ levels, and ensures portability through an ear-clip design. Validation includes: TC1 – sensor vs finger oximeter (<±2% deviation), TC2 – motion artefacts rejected by filtering/ML, TC3 – low-oxygen simulation triggers alerts, and TC4 – normal conditions show stable readings without false alarms.

## Slide 9
Conclusion & Future Work
Conclusion(So Far)
The literature survey confirms the need for continuous SpO₂ and heart-rate monitoring in low-ventilation environments.
Hardware components, including MAX3010x sensor and Arduino/ESP32, have been selected and finalized.
PPG data collection from volunteers has been completed, providing a foundation for ML analysis.
The project is feasible and promising for developing an ear-wearable monitoring device.
Summary of Work Completed
Literature survey and review of existing solutions.
Selection of hardware components for prototype.
Collection of initial PPG data.
Future Work
Run PPG data simulations and extract features for analysis.
Train ML models for noise removal and anomaly detection.
Assemble and test the ear-wearable prototype.
Evaluate device comfort and real-time alert system.
Optimize ergonomic design and consider wireless connectivity for supervisor monitoring.

## Slide 10
THANK YOU
Have a Great Day !